CONE WINDING SECTION

Stalking of Cones (base at bottom while nose at top- vice versa will result in slipping of yarn layers towards nose side during such a long time thus will result in defective packages )

Cone Adapters to be kept in lifted position but not riding over the expensive Bakelite Drums (apply anti-rust solution on Drums)

Electronic spares like Sensors, tensioners, clearers, invertors, etc and also rotating mechanical spares & bearings to be kept free of fluff

Tension belts of motors are of rubber –to be slackened & treated with oil inorder to avoid contraction & hardening of the same during the prolonged stop period ; as these items are continuously under tremendous pressure and stretch while working for 24 hrs in a day many times)

Remove expensive Lubricants and preserve them with care (especially those which are always in a circulation and active during the working of the machine; as these will lose its property/dried up in a prolonged stop)

Remove Waxing-units and preserve them to avoid from excessive fluff deposition

Hose tubes/pipes for pressure units (to be inspected for their condition while starting the machine after prolonged stop OR may be removed and preserved in a condition atmosphere)

Conveyor belts of Cone and Bobbin automatic systems OHTC, empty bobbin conveyor, package conveyor, Link Coner Feed conveyor, CBF round & link belt( to be relaxed from tension for avoiding them from getting hardened and contract

Drain complete air from the machine

All breakers including (AD & CBF) to be switched off