WARPING  SECTION

Stalking of Cones (base at bottom while nose at top- vice versa will result in slipping of yarn layers towards nose side during such a long time thus will result in defective packages )

Tension belts of motors are of rubber –to be slackened & treated with oil inorder to avoid contraction & hardening of the same during the prolonged stop period ; as these items are continuously under tremendous pressure and stretch while working for 24 hrs in a day many times Also Belts of Motor of Ventilated Disc Brakes

Remove expensive Lubricants and preserve them with care (especially those of Centralized Lubrication system which are always in a circulation and active during the working of the machine; as these will lose its property/dried up in a prolonged stop)

Remove empty or ½ wounded beams and preserve properly along with the cheese and cones of the Creel away from fluff

Apply anti-rust oil to Comb Dents

Release Hydraulic brakes, remove oil and release pressure

Hose tubes/pipes for pressure units (to be inspected for their condition while starting the machine after prolonged stop OR may be removed and preserved in a condition atmosphere)

Care to be taken that items like Mechanical, Electronic, Optic feelers, tensioners, yarn detectors are covered properly avoiding from fluff accumulation/deposition

Preserve/cover properly the friction drum of head stock as its surface is very important

Care to be taken that rubber package holders of the Creel doesn’t get hardened during the prolonged stop and loses its property of tightly holding the Cones/Cheeses mounted over them – may be applied oil