SIZING  SECTION

Drive Zone (Head Stock) Comb Dents with anti-rust solution PIV Gears properly covered Incomplete sized beams to be removed and preserved properly from white ants (due to size)

Dry Zone (Cylinders) Drying Cylinders to be properly covered to preserve the costly Teflon coating Remove the accumulated water inside the Cylinders Sprocket chains if slackened may help

Wet Zone (Size Box) Empty size box, clean and keep it full with water-it will help in avoiding the blocking up of holes of steam pipe by the fluff if kept exposed to the atmosphere(preserve the size properly) Squeeze Rollers to be preserved properly as its Shore hardness may be affected due to its property of constantly exposed to high temperatures @ 90 degrees during squeezing action Squeeze and Immersion Rollers to be kept lifted and away from each other’s contact Bearings to be properly covered to avoid fluff blockage

Creel Zone Brakes to be cleaned and properly covered Incomplete warper beams to be removed and preserved properly